## Slide 1
Computational Thinking - Fall 2024
16-Bit CPU Design
Created By Ali Shah (ERP 31626)

## Slide 2
Core Architecture

## Slide 3
Memory Address Registers
Memory Buffer Registers
Input and Output Registers
Random Access Memory
Program Control Unit
Arithmetic Logic Unit
Program and Clock Counter
Bus Terminal
Instruction Decoder

## Slide 4
Operations

## Slide 5
Arithmetic: Add, Subtract, Multiply
Logical: AND, XOR, NOT
Compare: Lesser, Equal, Greater
Storage: Result and Overflow
Swap: Memory or Registers
Matrix: Load, Multiply, Store
Debug: Delay
Others: Reserved, NOP, Halt

## Slide 6
Data Flow

## Slide 7
Program counter contains the instruction address.
The address is transferred and stored in MAR Zero.
Data in instruction RAM is accessed at that address.
Instruction (data from RAM) is stored in MBR Zero.
Instruction is split into opcode, flag, and addresses. The opcode and flag are stored in registers, address A is stored in MAR A, and address B in MAR B.
Clock counter is reset to 0.
The instruction is executed.
Program counter increments by 1.
Order may vary due to pipelining (discussed later).
Fetch Decode Execute Cycle

## Slide 8
Highlight

## Slide 9
3.38
On Average,
Clock Cycles

## Slide 10
How?

## Slide 11
Pipelining

## Slide 12
When executing the current instruction, the next instruction is fetched and stored into MBR Zero.
At last execution step, the instruction is sent from MBR to instruction splitter.
The opcode, flag, and two addresses are stored and next instruction begins.

## Slide 13
Moreover, before the execution of the current instruction ends, the address of the next-to-next instruction is fetched and stored into the MAR Zero.
These techniques reduce the number of clock cycles and make the design more efficient as the next instructions are fetched and decoded during execution.

## Slide 14
Operations, classified by clock cycles:
2 Cycles: Reserved, Debug, NOP/Halt
3 Cycles: Add/Subtract, Multiply, Compare, AND, XOR, NOT, Register Swap, Memory Swap
4 Clock Cycles: Store, Mat Mult, Move
5 Clock Cycles: Block Load
7 Cycles: Block Store

## Slide 15
PCU Design

## Slide 16
The PCU was designed by first creating an automated Excel workbook.
The workbook contains sheets with a truth table for each type of operation.
Truth tables can be converted into binary or hexadecimal to provide the final contents to be stored in the PCU.

## Slide 17
The workbook also tracks the clock cycles for each of the operations.
The ‘Scripts’ sheet can be used to convert an instruction in English and base 10 into binary or hexadecimal.
The ‘Operations’ sheet tracks each of the operations classified into types.

## Slide 18
Additional
Features

## Slide 19
The program is automatically halted when the all instructions stored in the instruction RAM have been executed.
The block store operation can store the overflow in the matrix multiplication result when the flag is set to 1.

## Slide 20
LED displays and probes have been added in the circuit to make dry running and debugging easier.